## Slide 1
Toward SDN for Tactical Edge Networks Y. Richard Yang Yale University

## Slide 2: What is SDN?
Separation of data and control paths
Logically centralized control plan
…
Notes:   Risk: having a narrowly defined hammer and looking for nails

## Slide 3: A More General View of SDN: Programmable Networks
    Same deployed (physical) asset
    Programmability to
      provide more functions
      utilize asset more efficiently

## Slide 4: SDN Progress as Programmability Progress
Network State
Datapath Model/ Program
Service/ Policy
Datapath Model/ Program
Program Logic
OpenFlow => P4/POF
Distributed Comp => Logically Centralized Comp
Low-level Programming => High-level Programming

## Slide 5: High-level SDN Programming Abstraction: Function Store
function instance
public void QoSRouting(Ipv4Address src, Ipv4Address dst, int requiredBw) {
srcNode, dstNode = mapToNode(src, dst);
topology = readTopology();
pq.add(srcNode);
while (!pq.isEmpty()) {
n = pq.pop();
if (bw_src(n) < requiredBw)
return failure
if (n == dstNode)
return writeRoute(src, dst, path);
for (e(n->m): n.neighbors) {
if (min(e.bw, bw_src(n)) > bw_src(m)) {
updateBw(m, min(e.bw, bw_src(n)));
...
}
}
}
return failure }
    Allow generic functions
    Automatically track data dependency
    Automatic clean up, reschedule, and re-execute after dependent data changes (achieve intent)
function instance
function instance

## Slide 6: High-level SDN Programming Abstraction: Magellan
Consider each pkt as a request
- Network as a single virtual server
- Network functions (logically) invoked on each new pkt, returning how net handles that request
- Network functions expressed in general purpose language
- Realization of return is opaque, computed by system

## Slide 7: Example Magellan Program
void f(Packet p) {
if ( !permit(p) ) p.route = null;
else {
EndpointProp sedp = hostTable(p.ip.ipSrc());
EndpointProp dedp = hostTable(p.ip.ipDst());
int rate = p.te.vRate(); // custom protocol
QoSRoute qr = routingAlg(sedp, dedp, rate);
p.route = qr.route; p.vrate = qr.rate;
}
}
QoSRoute routingAlg(EndpointProp s, EndpointProp d, int r) {
if ( allowedRate(s, d) < r ) // authorization
r = allowedRate(s, d);
return QoSRouting(s, d, r);
}
Per-packet programming model
Standard+Custom protocols
Meta header to control cross layers
Unspecified realization: Source-routing, compile, or on-demand at switches
Notes: relatively low rate, unreliable, nodes are highly mobile

## Slide 8: Position Statement (I)
There has been substantial progress in the development of a systematic framework of SDN programming abstractions, e.g.,
  protocol oblivious programming
  high-level SDN programming allowing flexible, high-level, proactive/on-demand control
Tactical Edge Networks should consider leveraging the progress, to add flexibility, improve efficiency, and simplify control programming.
Notes: Protocol oblivious datapath and high-level SDN programming can lead to substantial flexibility and efficiency in network control and coordination

## Slide 9: Key Barrier
Control-Resource (CR) Channel: Capacity vs Demand
Tactical EdgeNet Resources (Network and Endhost Devices)
Control Plane
Notes: relatively low rate, unreliable, nodes are highly mobile

## Slide 10: Potential Way Forward: CR Channel-Adaptive Control and Programming
Tactical EdgeNet Resources (Network and Endhost Devices)
Control Plane
- Controlled mobility/asset to increase CR channel capacity
- Control channel embedding in data channel (aka fate sharing)
Approximate/coarse-grained CC (aka global + local CC)
Increase capacity
Decrease demand
- …
CRC adaptive realization (SR, C, OD)
Opportunistic CC benefits injection
- …
Notes: relatively low rate, unreliable, nodes are highly mobile

## Slide 11: Position Statement (II)
The Control-Resource channel can indeed be a key choking point, but bypass can exist
Key next step is to develop better understanding of the limit (aka SDN CR Capacity Theorem), evaluate the limit for key deployment settings
demand/capacity
Benefit

## Slide 12: Backup Slides

## Slide 13: Why Logically Centralized Control?
Inconsistent state
Arrow’s Impossibility Theorem
Notes: Inconsistent state is a key source of complexity

## Slide 14: Data Path Abstraction (OpenFlow)

## Slide 15: Data Store Abstraction (YANG)
https://wiki.opendaylight.org/view/OpenDaylight_Controller:Architectural_Framework

## Slide 16: Magellan Program to Command and Control
IR
Compile
Analyze&Optimize
Code Gen
Rules
Update
Datapath Design
“Oracle” Program
DB
onDemand Handler
Batch Explorer
Offline
Online
Network and Endhost Devices
Net State
Notes: relatively low rate, unreliable, nodes are highly mobile

## Slide 17: Network Forwarding as Caching Lookup
Central control function consists of a sequence of instructions I1, I2, …, In
Each instruction I is a mapping from input variable states to output variable states
InVar(I)1 | InVar(I)2 | InVar(I)3 | OutVar(I)
1 | 1 | 1 | OutVar(I)=I(1,1,1)
… |  |  | 
… |  |  | 
I
InVar(I)1
InVar(I)2
InVar(I)3
OutVar(I)